## Slide 1: Verification of the Flat Plate Natural Convection Model
Tue 1pm - Group 1
Luke Bailey, Alan Herbst, Randy Saintjean, Irving Zhang

## Slide 2: Content
Motivation & Background
DoE & Set up
Analysis & Results
Discussion
Future Directions and Improvements

## Slide 3: Motivation & Background
Heat transfer occurs via conduction, convection, radiation
Focus of this project: natural convection
Natural convection caused by buoyancy due to temperature gradients
Goal: experimentally estimate convection coefficient h
heat flux [W/m2]
ambient temperature [K]
surface temperature [K] ​
​
*As we are interested in the temperature gradient​, units of °C or K can be used, but cannot be mixed
​

## Slide 4: Design of Experiments
X1: Ts (hot plate temperature)
  Low: 60 °C
  High: 100 °C
X2: Box Size
  Low: Small
  High: Large (16"x20"x20")
X3: Angle of hot plate surface
  Low: 0° (flat/horizontal)
  High: 90° (vertical)

## Slide 5: Test Set up
Main System components
  insulated enclosure
    Air-sealed open-top cardboard box : low-cost, easy-setup option. Safe for low-temperatures.
    Custom wooden enclosure with double-pane setup was used for testing
  hot plate
  heat flux sensor
  thermocouple
  RTD
  Arduino + DAQ

## Slide 6: Sensors and Measurements
FluxTeq Compaq DAQ and PHFS-01
  Measure actual heat flux (W/m^2)
Watlow OKK30B10A
  Measure T_s (hot plate) (°C)
Adafruit PT100 RTD and MAX31865 Amplifier
  Measure T_∞ (ambient box temperature) (°C)

## Slide 7: DAQ & Analysis
Calibration
  RTD
    Submerge directly in ice bath – average offset based on series of readings
  OKK30B10A
    Enclose within plastic bag before submerging in ice bath (no liquid exposure) – average offset based on series of readings
  PHFS-01
    Attach to rated heater – average offset based on series of readings
    Two-hotplate, conduction "sandwich" method
What to collect
  RTD – T∞ [°C]
  OKK30B10A – Ts [°C]
  PHFS-01 – heat flux [W/m2 ]
How to analyze the data
  Compare calculated average convection coefficient for each factor combination to expected convection coefficient range with t-test (α=0.05)
    Left tailed test for lower bound of heat flux range
      Null hypothesis- h >= h_lower
      Alternative hypothesis- h< h_lower
    Right-tailed test for upper bound of heat flux range
      Null hypothesis- h <= h_upper
      Alternative hypothesis- h> h_upper
  Multiple Comparison Analysis (Dunn-Sidak) to determine which combinations are statistically different
  Main and Interaction Effects Full-Factorial Analysis

## Slide 8: Heat Transfer Model
Affects of other heat transfer modes
  Conduction and forced-convection:
    Negligible or not present within design
  Radiation:
    Non-negligible, must be accounted for
    Overlaying known low-emissivity Al. Foil (𝜀 = 0.03) enables radiative flux to be subtracted from measured flux
Bergman et al., Fundamentals of Heat and Mass Transfer 7ed, 2011
Bergman et al., Fundamentals of Heat and Mass Transfer 7ed, 2011

## Slide 9: Uncertainty
Design Stage
Zeroth Order
  Ts sensor Resolution: 0.25°C
  T∞ sensor Resolution: 0.03°C
  Heat flux sensor Res: ≈ 1.5 W/m^2
Dominant source: surface temperature (thermocouple)
Uncertainty ↑ when ΔT ↓
Thus, operate at larger temperature difference
Uho = 0.04 W/(m2K)
Uhd = 0.73 W/(m2K)​

## Slide 10: Sample Data
Chart: Temperature vs. Time
Chart: Flux vs. Time
Chart: h vs Time
Model confirmation!

## Slide 11: Discussion
Pros
  Easy to construct and adjust
    Cut and add cardboard
    Seal holes and gaps with duct putty
  Low cost
    Sensors readily available
  Removes air flow and outside disturbances
Cons
  Accounts for relatively few properties affecting convection
    Unaccounted for variations in convection coefficient
    Some variables affecting convection cannot be easily adjusted
      E.g. orientation of hot plate
  Irregular, time-sensitive temperature gradient
    Ambient temperature changes with distance from plate
    Temperature gradient will decrease over time
  Various influences on convection not isolated
Future work
  More flexible enclosure that allows for measuring more variables affecting convection
    E.g. heat plate orientation, geometry, flow characteristics

## Slide 12: Future Directions and Improvements
More flexible enclosure that allows for measuring and assessing additional convection-related variables
  E.g. heat plate orientation, geometry, flow characteristics
Improve measurement quality
  E.g. ensure flat, complete contact between plate + foil and foil + sensors
Fully-enclose the system to assess dynamics of time-varying temperature gradient
Generalize and apply approach to common engineering designs
  Measuring and optimizing h-values may improve common products
    Electronics (desktop PCs), ovens, radiators, building design/cooling, etc.

## Slide 13: Appendix & Credits
References:
Cengel and Boles, Thermodynamics: An Engineering Approach, 5th edition, McGraw-Hill, 2006.
Bergman, Lavine, Incropera, and Dewitt, Fundamentals of Heat and Mass Transfer, 7th Edition, John Wiley and Sons, 2011
Vipperman, J., “Lab 2 Handout - Insulation R-Value of Single-Pane and Dual-Pane Windows”, University of Pittsburgh, 2026.
Arduino, "Adafruit MAX 31855 library," Arduino Documentation, Nov., 15, 2023
Arduino, "Adafruit MAX 31865 library," Arduino Documentation,Nov., 15, 2023